## Slide 1: A Practical Approach to the Year 2038 problem for 32bit Embedded Systems
Hideyuki Oe Osaka University
Asia BSD CON 2020
Makoto Matsushita, Katsuro Inoue Osaka University

## Slide 2: Outline
Introduction
Method
Results
Conclusion
Discussions
Future Works

## Slide 3: Introduction

## Slide 4: Introduction What is the year 2038 problem ?
January 19, 2038, 3 o’clock
14 minutes 7 seconds
January 19, 2038, 3 o’clock
14 minutes 8 seconds
January 19, 2038, 3 o’clock
14 minutes 7 seconds
January 1st, 1970, 0 o’clock
0 minutes 0 seconds*
Actual time (UTC)
System time (UTC)
This lead to the problem like the year 2000 problem.
* An example of invalid time value.

## Slide 5: Introduction How does this problem occur ?
Digit overflow occurs in the year 2038, because of the type “time_t” is defined by “32bit signed int” type in the 32bit system.
January 1st, 1970, 0 o’clock 0 minutes 0 seconds (Epoch)
time_t-type value
0x00000000
January 19, 2038, 3 o’clock 14 minutes 7 seconds
time_t-type value
0x7FFFFFFF
January 19, 2038, 3 o’clock 14 minutes 8 seconds
time_t-type value
0x80000000
A system might misunderstand the current time.
Time value is handled by “time_t”

## Slide 6: Our Method

## Slide 7: Method An example of the target system
Time value from outside
(broad cast signal)
Display the drawing items.
TV Program, On Screen Display, …
If the system timer returns to 1970 …
This photograph is an image

## Slide 8: Method Our target system
Drawing material
(including time information)
(From other device)
Drawing material
Input device
(operation)
System time
Drawing decision
Append, delete
Current time
Drawing command
Data for display
Data flow
Control flow
Development target system
Display device
Drawing material
(including time information)
20 years warranty
Keep it up after 2038

## Slide 9: Method Our software architecture
Kernel／Driver
UNIX base system (OS core)
init
UNiX
command
File system
Device driver
Boot
Boot loader
Library
Daemon
Application layer
Drawing engine
Communication
Data conversion
Data storage
Reshape drawing
Display control
User I/F
Function management
A
B
A : In-house development part, B : OS part
1.3
Million lines
0.5
Million lines

## Slide 10: Method The number of changes in the program
Location | Number of changes
OS part (including device driver, OSS, standard library) | 2546
In-house development part | 945
We did not want to modify the OS part, because…
The modification volume is huge for the development period.
The maintenance cost of modification would be expensive.

## Slide 11: Method Possible Solutions
32bit
64bit
・・・
・・・
Overflow?
time += 68years
y
n
1970
2038
1998
2066
(a) 64-bit time_t or change to 64-bit OS
(b) Unsigned int time_t
32bit
bit0
bit31
Use the sign bit for the time value
・・・
(c) Check the digit overflow and treat it
in the program.
(d) Change the “epoch”
About 68 years
Over 290 billion years
About 136 years
About 68 years
About 68 years

## Slide 12: Method Our design decision
Approaches | Development volume | OS part modify | Impact range
(a) 64-bit time_t or change to 64-bit OS. | Huge | Needed | Huge
(b) Unsigned int time_t. | Huge | Needed | Huge
(c) Check the digit overflow and treat it in the program. | Huge | Needed | Huge
(d) Change the “epoch”. | Medium | Unnecessary | Medium

## Slide 13: Method Our design
How many years we have to shift from 1970(epoch) ?
How do we shift the epoch ?
Which kind of data do we have to check ?
Which kind of library functions do we have to check ?
We can get the design of the program.

## Slide 14: Method Change the epoch from 1970 to 1998
January 1, 1970
0:00:00
Date and time（UTC）
Epoch (1970)
Epoch (1998)
0x0000 0000
－
January 1, 1998
0:00:00
0x34AA DC80
0x0000 0000
January 19, 2038
3:14:07
0x7FFF FFFF
0x4B55 237F
January 19, 2066
3:14:07
0xB4AA DC7F
0x7FFF FFFF
(time_t type variable value)
28 years shift because
20 years warranty (need to shift over 20 years)
Multiples of 4 to account for leap years
No need to calculate the “day of week” until the year 2099

## Slide 15: Method Calendar every 28 years
Su | Mo | Tu | We | Th | Fr | Sa
1 | 2 | 3 | 4 | 5 | 6 | 7
8 | 9 | 10 | 11 | 12 | 13 | 14
15 | 16 | 17 | 18 | 19 | 20 | 21
22 | 23 | 24 | 25 | 26 | 27 | 28
29 | 30 | 31 |  |  |  | 
Su | Mo | Tu | We | Th | Fr | Sa
1 | 2 | 3 | 4 | 5 | 6 | 7
8 | 9 | 10 | 11 | 12 | 13 | 14
15 | 16 | 17 | 18 | 19 | 20 | 21
22 | 23 | 24 | 25 | 26 | 27 | 28
29 | 30 | 31 |  |  |  | 
Su | Mo | Tu | We | Th | Fr | Sa
1 | 2 | 3 | 4 | 5 | 6 | 7
8 | 9 | 10 | 11 | 12 | 13 | 14
15 | 16 | 17 | 18 | 19 | 20 | 21
22 | 23 | 24 | 25 | 26 | 27 | 28
29 | 30 | 31 |  |  |  | 
March, 2048
March, 2076
March, 2020
28 years
28 years

## Slide 16: Method Change the epoch mechanism
Epoch interpretation change
time value (except time_t type variable)
time_t type variable
(1998 Epoch)
Library
(1970 epoch)
time_t type variable
(1998 Epoch)
Change epoch
between 1970 and 1998
After modification
External time value
A
B
time value (except time_t type variable)
time_t type variable
(1970 Epoch)
Library
(1970 epoch)
time_t type variable
(1970 Epoch)
Before modification
External time value
Data flow
(Do not change epoch)
(Change epoch)
A
B
A : In-house development part
B : OS part
Do not change this part.

## Slide 17: Method The data types which need to check
Number | Types | Abstraction
1 | time_t | Data type for storing system time. It is defined in the standard C library, and is defined as 32-bit signed integer in 32-bit FreeBSD.
2 | struct timeval | A structure that has a time_t-type variable (tv_sec) and a suseconds_t-type variable (tv_usec) as members. tv_sec stores seconds, and tv_usec stores microseconds.
3 | struct tm | A structure that stores time information for each element such as year, month, day, day of the week as members, and stores each member as an int.

## Slide 18: Method The library function examples
Number | Function name | Wrapper function creation
1 | clock_t clock(void) | ―
2 | char *ctime(const time_t *) | Required
3 | double difftime(time_t, time_t) | ―
4 | int gettimeofday(struct timeval *, struct timezone *) | Required
5 | struct tm *gmtime(const time_t *) | Required
6 | struct tm *localtime(const time_t *, struct tm *) | Required
7 | time_t mktime(struct tm *) | Required
8 | int settimeofday(const struct timeval *, const struct timezone *) | Required
9 | time_t timegm(struct tm *) | Required
・ | ・ | ・
・ | ・ | ・
60 | void tzsetwall(void) | ―

## Slide 19: Method The time value’s data flow and control flow
System time
settimeofday
Application
getttimeofday
Epoch(1970) time
CTIME functions
(localetime_r etc.）
Present time
Control flow
Data flow
Device driver
・・・
OS part
Original system

## Slide 20: Method How to change the epoch
Device driver
・・・
OS part
System time
settimeofday
wrapper_settimeofday
Application
Decrease 28 years
wrapper_getttimeofday
getttimeofday
Epoch(1998) time
CTIME functions
(localetime_r etc.）
CTIME wrapper functions
(wrapper_localetime_r etc.）
Do not change the year value
Increase 28 years
Present time
Calculate time : before 28 years
Control flow
Epoch(1998) time
Epoch(1970) time

## Slide 21: Implementation

## Slide 22: Implementation Macro definition
#define DATE_OFFSET_YEAR 28 /* 28years */
#define LEAP_DAYS (DATE_OFFSET_YEAR >> 2)
#define DATE_OFFSET_SEC ((DATE_OFFSET_YEAR * 365 + LEAP_DAYS) * 60 * 60 * 24)
・・・

## Slide 23: Implementation Wrapper function (1)
int wrapper_settimeofday(const wrapper_timeval * tv , const struct timezone * tz)
{
struct timeval tv_tmp, *tvp;
int ret;
if (NULL == tv)
{
tvp = NULL;
}
else {
tv_tmp.tv_sec = (time_t)(tv->tv_sec - DATE_OFFSET_SEC);
tv_tmp.tv_usec = tv->tv_usec;
tvp = &tv_tmp;
}
ret = settimeofday(tvp, tz);
return ret;
}

## Slide 24: Implementation Wrapper function (2)
struct tm* wrapper_localtime_r (const time_t *clock, struct tm *result)
{
struct tm *tm_tmp;
if ((tm_tmp = localtime_r(clock, result)) != NULL)
{
result->tm_year += DATE_OFFSET_YEAR;
}
return tm_tmp;
}

## Slide 25: Results

## Slide 26: Result The number of the test items and results
 | Test items | Number of defects
Unit test | 165 | 0
Integrated test | 103 | 1

## Slide 27: Result The modification volume
 | Library function name | Created lines of wrapper function | Number of call locations | Modification lines of calling part
1 | ctime | 11 | 0 | 0
2 | ctime_r | 11 | 0 | 0
3 | gettimeofday | 6 | 25 | 1262
4 | gmtime | 9 | 0 | 0
5 | gmtime_r | 9 | 1 | 21
6 | localtime | 9 | 2 | 12
7 | localtime_r | 9 | 30 | 1131
8 | mktime | 22 | 10 | 307
9 | settimeofday | 15 | 2 | 127
10 | strftime | 81 | 2 | 48
11 | timegm | 22 | 1 | 28
12 | timelocal | 22 | 0 | 0
13 | Common functions etc.* | 38 | - | -
Total |  | 264 | 73 | 2936
Modification lines |  | 264 + 2936 = 3200 |  | 
* Includes functions shared by multiple wrapper functions and “include” and “define” statements.

## Slide 28: Result Calculation of the “man-months”
Development efficiency in all project processes = 3.45 steps / man-hours
Correction volume = 3200 steps
Development efficiency in the “year2038 problem” = 3200 / 3.45 = 927.54 man-hours
8 hours / day, 20 days / month
927.54 / (8 * 20) = 5.80 man-months

## Slide 29: Discussions

## Slide 30: Discussions Evaluation of corrective work
Project
Development was completed as planned
There was nothing particularly difficult
Method
The new system cannot handle before 1998
Easy solution by changing epoch (from 1970 to 1998) by wrapper functions

## Slide 31: Related Issues

## Slide 32: Related Issues Handling date and time in Software
 | Windows | NetBSD | macOS/iOS | FreeBSD | Raspbian
Time info | 64bit | 64bit | 64bit | 64bit/32bit | 32bit
Remarks | In versions of Visual C++ and Microsoft C/C++ before Visual Studio 2005, time_t was a long int (32 bits). | NetBSD has been modified to represent time_t in 64 bits on all supported architectures. | Time is expressed as the number of seconds since January 1st, 2001 UTC, and it is currently defined by regulations to allow only 64-bit applications. | The 32-bit OS can be used continuously, but the 2038 problem described in this paper will occur. | Raspbian Buster has released on 2020-02-13, but still 32-bit system.

## Slide 33: Related Issues The UNIX’s year 2004 issues
1970
2004
2038
Digit overflow occurred because …
Two dates are added together
0.5sec unit timer
0x0000 0000
0x4000 0000
0x7FFF FFFF
13:37:04, January 10th, 2004(UTC)

## Slide 34: Related Issues The year 2000 problem
1
9
9
9
2
0
0
0
(a) The time period calculation
(b) Comparison which is newer
(c) Newer data save logic
No major confusion occurred because prior approaches.
Ex) From the year 1996 till 2000 is “00 – 96 = -96” ?
Ex) The year 1996 is newer than the year 2000 because “96 > 00” ?
Ex) Save the year 1999 data and delete the year 2000 data because “99 > 00” ?
Use only 2 digits for represent the year

## Slide 35: Conclusion and Future Works

## Slide 36: Conclusion
shifting the epoch from 1970 to 1998 with wrapper functions
- Development of the 20 years warranty products
- Considering the leap year
- No need to calculate the week of days
We have solved the year 2038 problem without modify the OS part by
in 32-bit FreeBSD system.
The modification cost was 5.80 man-month for 1.3 million lines application.

## Slide 37: Future Works
So many systems are working in the 32-bit system now.
For example “Raspbian” is a popular OS, for the inexpensive IoT systems.
We’d like to solve the year 2038 problems more efficiently.
The impact may be greater than we think…
Some IoT systems that include this problem may run beyond 2038 invisibly.

## Slide 38: Acknowledgement
We deeply appreciate the developers of 2nd Engineering Department at Persol AVC Technology Co., Ltd. for providing data related to this project.
Thank you very much

## Slide 39: References
Brown, E.: Embedded Linux Keeps Growing Amid IoT Disruption, Says Study, Linux.com News, 2015.
Apple: 64-bit Transition on macOS, Apple Developers News and Update, https://developer.apple.com/news /?id=0411018a, April 11, 2018.
FreeBSD: time(3), FreeBSD 11.1-RELEASE manual, 2003.
Holzmann, G.: Out of Bounds, IEEE Software, Vol32, No.6, pp24-26, 2015.
Takatomo Suzuki, Kensuke Nakamura : Troubles in “year 2038 problem”, Nikkei Computer (2004-4-1), http://tech.nikkeibp.co.jp/it/ members/NC/ITARTICLE/20040325/1/, 2004 (in Japanese).
Takao Yokota : Meaning of the year 2000 problem and countermeasures, Computer Software, Vol.13, No.5, pp.412-419, 1996 (in Japanese).
Cabinet Computer Year 2000 Problem Management Office, “Report on the year 2000 problem”, https://www.kantei.go.jp/jp/pc2000/ houkokusyo/honbun.html, 2000 (in Japanese).
Harshini, S. and Kavyasri, K. R.: Digital World Bug : Y2k38 an Integer Overflow Threat-Epoch, International Journal of Computer Sciences and Engineering, Vol.5(3), Mar 2017, E-ISSN : 2347-2693 , 2017.
Microsoft: Microsoft Docs: Time Management, https:// docs.microsoft.com/en-us/cpp/c-runtime-library/time-management
Apple: NSDate - Foundation | Apple Developer Documentation, https://developer.apple.com/documentation/foundation/nsdate
Apple: 64-bit Requirement for Mac Apps, https://developer.apple.com/ news/?id=06282017a
Apple: 64-bit Apps on iOS 11, https://developer.apple.com/ news/?id=06282017b
NetBSD Foundation: Announcing NetBSD 6.0, https:// www.netbsd.org/releases/formal-6/NetBSD-6.0.html